## Slide 1
NON-WSQ COURSE
Semiconductor Process Fundamentals Masterclass
Connect modules · control interactions · verify device performance
C716
Version v1.0 · 1 October 2026
Trainer: Dr Alfred Ang
Tertiary Infotech Academy Pte Ltd · UEN 201200696W

## Slide 2
TRAINER PROFILE
About the Trainer - General Template
?
Your Trainer
Complete before delivery
NAME
________________________________________
TITLE / DESIGNATION
________________________________________
QUALIFICATIONS
________________________________________
AREAS OF EXPERTISE
________________________________________
TRAINING EXPERIENCE
________________________________________
CONTACT
________________________________________
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
2

## Slide 3
TRAINER PROFILE
About the Trainer - Dr Alfred Ang
AA
Dr Alfred Ang
Principal Trainer
ROLE
Principal Trainer
QUALIFICATIONS
Doctorate · ACTA/ACLP-aligned adult educator
EXPERTISE
Semiconductor · quality · emerging technology
EXPERIENCE
Professional training and technology leadership
CONTACT
enquiry@tertiaryinfotech.com
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
3

## Slide 4
ICEBREAKER
Let's Know Each Other
1
Name, organisation and role
2
Your semiconductor process or quality experience
3
One module interaction you find difficult
4
One result you want by the end of Day 2
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
4

## Slide 5
HOUSEKEEPING
Ground Rules
1
Evidence first
distinguish measurements from assumptions
2
Participate actively and ask technical questions
Participate actively and ask technical questions
3
Respect confidential process and product information
Respect confidential process and product information
4
One conversation at a time
One conversation at a time
5
Return from breaks punctually
Return from breaks punctually
6
Stop any unsafe or unauthorised activity
Stop any unsafe or unauthorised activity
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
5

## Slide 6
COURSE AT A GLANCE
Course Profile
Programme
1
2 days · 15 hours
2
Course code: C716
3
9:30am–5:30pm · 7.5 hours per day
4
Topic 1: process flow
Evidence and practice
1
Topic 2: integration and performance
2
Eight individual activity folders
3
Worksheets, checklists and evidence records
4
Course synthesis on Day 2
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
6

## Slide 7
SCHEDULE
Lesson Plan - Day 1
Morning
1
09:30 Introductions and course overview
2
09:50 Block 1A: patterning and etch
3
10:55 Activities 1-2
4
12:40 Lunch
Afternoon
1
13:10 Block 1B: implant, thermal and films
2
14:30 Activities 3-4
3
16:20 Integrated-flow review
4
17:30 End of Day 1
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
7

## Slide 8
SCHEDULE
Lesson Plan - Day 2
Morning
1
09:30 Day 1 retrieval; Block 2A: performance, yield and reliability
2
11:20 Activity 5
3
12:20 Lunch
4
12:50 Activity 6
Afternoon
1
14:05 Block 2B: SPC and packaging
2
15:20 Activities 7-8
3
17:00 Course synthesis and feedback
4
17:30 End of class
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
8

## Slide 9
LEARNER MATERIALS
Access the Course Activities
↗
Open the course repository to access all eight activity folders.
Detailed download and file-access guidance is provided in the Learner Guide.
https://github.com/tertiarycourses/C716-Semiconductor-Process-Fundamentals-Masterclass
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
9

## Slide 10
PROCESS-INTEGRATION MINDSET
A fab is a connected system, not a collection of tools.
Every module hands variation, defects and evidence to the next module.
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
10

## Slide 11
TOPIC 1 · LEARNING BLOCK 1A
Patterning, Etch and Fab Control
Build reliable patterns while controlling contamination, CD, overlay and profile.
1A
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
11

## Slide 12
PART 1 · BUILD THE MODEL
Block 1A Roadmap
1
The Wafer Fab as a System
The Wafer Fab as a System
2
Contamination Has Multiple Pathways
Contamination Has Multiple Pathways
3
The Lithography Stack
The Lithography Stack
4
Mask Tone and Resist Tone
Mask Tone and Resist Tone
5
Resist Coating and Bake
Resist Coating and Bake
6
Resolution, NA and Process Margin
Resolution, NA and Process Margin
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
12

## Slide 13
PART 2 · VERIFY THE EVIDENCE
Block 1A Roadmap
1
Overlay, OPC and Mask Protection
Overlay, OPC and Mask Protection
2
Wet Etch versus Dry Etch
Wet Etch versus Dry Etch
3
Etch Selectivity and Profile
Etch Selectivity and Profile
4
Strip and Clean
Strip and Clean
5
Pattern-Transfer Window
Pattern-Transfer Window
6
Patterning Evidence Gate
Patterning Evidence Gate
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
13

## Slide 14
BLOCK 1A · IMAGEGEN VISUAL
Patterning, Etch and Fab Control in Practice
1
What module is creating the feature?
2
Which interaction can move device performance?
3
What measurement makes the decision defensible?
4
Where should feedback or containment occur?
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
14

## Slide 15
LEARNING BLOCK 1A · TOPIC 1
The Wafer Fab as a System
1
Product flow
hundreds of tightly coupled operations
2
Cleanroom
particles and molecular contamination are controlled
3
Integration
each module owns incoming and outgoing evidence
4
Release logic
a pass is a measured decision, not an assumption
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
15

## Slide 16
LEARNING BLOCK 1A · TOPIC 1
Contamination Has Multiple Pathways
1
Particles
block patterns and create opens or shorts
2
Ions
shift electrical behaviour and junction properties
3
Organics
interfere with adhesion, exposure and interfaces
4
Water and tools
transport hidden contamination between modules
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
16

## Slide 17
LEARNING BLOCK 1A · TOPIC 1
The Lithography Stack
WHAT CHANGES
1
Mask or reticle carries the intended geometry
2
Resist converts optical energy into a soluble contrast
WHAT TO VERIFY
1
Alignment connects the current level to prior levels
2
Developed resist becomes the etch or implant mask
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
17

## Slide 18
LEARNING BLOCK 1A · TOPIC 1
Mask Tone and Resist Tone
1
Clear-field and dark-field masks invert where light passes
Clear-field and dark-field masks invert where light passes
2
Positive resist removes exposed regions
Positive resist removes exposed regions
3
Negative resist retains exposed regions
Negative resist retains exposed regions
4
The combination determines whether a hole or island remains
The combination determines whether a hole or island remains
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
18

## Slide 19
LEARNING BLOCK 1A · TOPIC 1
Resist Coating and Bake
1
Prime improves adhesion on the prepared surface
Prime improves adhesion on the prepared surface
2
Spin speed and dispense control resist thickness
Spin speed and dispense control resist thickness
3
Soft bake removes solvent without damaging image response
Soft bake removes solvent without damaging image response
4
Edge bead and coverage affect focus and defectivity
Edge bead and coverage affect focus and defectivity
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
19

## Slide 20
LEARNING BLOCK 1A · TOPIC 1
Resolution, NA and Process Margin
Wavelength
shorter light supports smaller features
Numerical aperture
higher NA improves resolution
Depth of focus
normally shrinks as NA rises
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
20

## Slide 21
LEARNING BLOCK 1A · TOPIC 1
Overlay, OPC and Mask Protection
1
Overlay error shifts one layer against another
Overlay error shifts one layer against another
2
OPC pre-distorts features to counter imaging effects
OPC pre-distorts features to counter imaging effects
3
Antireflective layers reduce standing-wave effects
Antireflective layers reduce standing-wave effects
4
Pellicles and inspection reduce repeating defects
Pellicles and inspection reduce repeating defects
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
21

## Slide 22
LEARNING BLOCK 1A · TOPIC 1
Wet Etch versus Dry Etch
WHAT CHANGES
1
Wet etch is often isotropic and can undercut
2
Plasma/RIE supports directional profiles
WHAT TO VERIFY
1
Chemistry controls material reaction
2
Bias, pressure and transport influence sidewalls and damage
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
22

## Slide 23
LEARNING BLOCK 1A · TOPIC 1
Etch Selectivity and Profile
1
Selectivity protects resist and stop layers
Selectivity protects resist and stop layers
2
Over-etch clears residual film but consumes margin
Over-etch clears residual film but consumes margin
3
Microloading makes local pattern density matter
Microloading makes local pattern density matter
4
Endpoint and cross-section evidence localise failure
Endpoint and cross-section evidence localise failure
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
23

## Slide 24
LEARNING BLOCK 1A · TOPIC 1
Strip and Clean
1
Wet strip dissolves resist where surfaces tolerate chemistry
Wet strip dissolves resist where surfaces tolerate chemistry
2
Dry strip removes organics but can damage sensitive layers
Dry strip removes organics but can damage sensitive layers
3
RCA-type cleans target particles, organics and metals
RCA-type cleans target particles, organics and metals
4
Drying must avoid watermarking and recontamination
Drying must avoid watermarking and recontamination
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
24

## Slide 25
LEARNING BLOCK 1A · TOPIC 1
Pattern-Transfer Window
Lithography CD sets the incoming geometry
Lithography CD sets the incoming geometry
Etch bias changes the final feature
Etch bias changes the final feature
Across-wafer signatures expose non-uniformity
Across-wafer signatures expose non-uniformity
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
25

## Slide 26
LEARNING BLOCK 1A · TOPIC 1
Patterning Evidence Gate
1
Geometry
CD, overlay and profile
2
Defects
bridge, open, pinhole, residue or collapse
3
Mechanism
exposure, develop, etch or clean
4
Action
release, conditional release, hold or scrap
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
26

## Slide 27
LEGACY VISUAL · SOURCE SLIDE 23
Photolithography Exposure Geometry
READ THE VISUAL
1
Trace light from source through the mask
2
Connect the aerial image to resist contrast
3
Identify the alignment reference
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
27

## Slide 28
LEGACY VISUAL · SOURCE SLIDE 74
Etch Profile and Undercut
READ THE VISUAL
1
Compare anisotropic and isotropic profiles
2
Locate the material at risk during over-etch
3
Link sidewall shape to selectivity and transport
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
28

## Slide 29
LEGACY VISUAL · SOURCE SLIDE 104
Damage Recovery and Dopant Activation
READ THE VISUAL
1
Separate crystal repair from electrical activation
2
Recognise diffusion during the thermal cycle
3
Relate the result to later junction performance
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
29

## Slide 30
LEGACY VISUAL · SOURCE SLIDE 143
Dual-Damascene Integration
READ THE VISUAL
1
Follow via and trench formation
2
Locate barrier, seed and copper fill
3
Identify where CMP closes the module
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
30

## Slide 31
LEARNING BLOCK 1A · REAL-USE-CASE ACTIVITY
Build a CMOS Process Module Map
ACTIVITY 1
A new 300 mm logic product is moving from process development into a pilot manufacturing line. The integration team needs one agreed process map before module owners set recipes and control plans.
YOU'LL PRODUCE
Organise the legacy module coverage into a defensible FEOL-to-BEOL flow and expose the interfaces that can propagate variation.
Full procedure: Learner Guide and individual activity folder
LO1 · 45 minutes
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
31

## Slide 32
ACTIVITY 1 · ANALYSE BEFORE DECIDING
Visual Brief and Evidence Lens
1
Which module interaction is most critical?
2
What evidence distinguishes competing causes?
3
Where is the hold/release gate?
4
What follow-up action closes the risk?
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
32

## Slide 33
ACTIVITY 1 · VERIFY
Acceptance Review
✓
The map contains all seven key process modules and distinguishes FEOL from BEOL.
✓
At least eight process hand-offs have a measurable characteristic.
✓
At least three control/feedback loops and two cross-module interactions are justified.
Evidence: analysis output · completed checklist · measurement trail · decision and owner
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
33

## Slide 34
LEARNING BLOCK 1A · REAL-USE-CASE ACTIVITY
Diagnose a Pattern-Transfer Process Window
ACTIVITY 2
A contact layer shows intermittent bridging and open defects. Lithography CD, resist profile and plasma-etch selectivity must be reviewed together rather than as isolated module results.
YOU'LL PRODUCE
Connect mask/resist/exposure decisions to etch profile and select a stable corrective action without masking the root cause.
Full procedure: Learner Guide and individual activity folder
LO1 · 60 minutes
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
34

## Slide 35
ACTIVITY 2 · ANALYSE BEFORE DECIDING
Visual Brief and Evidence Lens
1
Which module interaction is most critical?
2
What evidence distinguishes competing causes?
3
Where is the hold/release gate?
4
What follow-up action closes the risk?
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
35

## Slide 36
ACTIVITY 2 · VERIFY
Acceptance Review
✓
Every defect is linked to a plausible lithography/etch mechanism.
✓
The dominant CD-shift stage is supported by before/after evidence.
✓
Corrective levers include predicted benefit, risk and verification measurement.
Evidence: analysis output · completed checklist · measurement trail · decision and owner
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
36

## Slide 37
CHECK YOUR UNDERSTANDING
Block 1A Recap
1
Explain
Etch Selectivity and Profile
2
Explain
Strip and Clean
3
Explain
Pattern-Transfer Window
4
Explain
Patterning Evidence Gate
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
37

## Slide 38
Lunch Break
45 minutes
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
38

## Slide 39
TOPIC 1 · LEARNING BLOCK 1B
Implant, Thermal, Films and Integrated Flow
Control material modification, film formation, planarity and FEOL-to-BEOL hand-offs.
1B
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
39

## Slide 40
PART 1 · BUILD THE MODEL
Block 1B Roadmap
1
Implant Dose and Energy
Implant Dose and Energy
2
Beamline Risks
Beamline Risks
3
Crystal Damage and Activation
Crystal Damage and Activation
4
Diffusion, Furnace and RTP
Diffusion, Furnace and RTP
5
Thermal Oxidation
Thermal Oxidation
6
CVD, PECVD and Epitaxy
CVD, PECVD and Epitaxy
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
40

## Slide 41
PART 2 · VERIFY THE EVIDENCE
Block 1B Roadmap
1
PVD, Barrier and Seed
PVD, Barrier and Seed
2
Copper Dual Damascene
Copper Dual Damascene
3
CMP Mechanics and Chemistry
CMP Mechanics and Chemistry
4
Planarity Failure Modes
Planarity Failure Modes
5
Integrated FEOL and BEOL
Integrated FEOL and BEOL
6
Cross-Module Budgeting
Cross-Module Budgeting
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
41

## Slide 42
BLOCK 1B · IMAGEGEN VISUAL
Implant, Thermal, Films and Integrated Flow in Practice
1
What module is creating the feature?
2
Which interaction can move device performance?
3
What measurement makes the decision defensible?
4
Where should feedback or containment occur?
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
42

## Slide 43
LEARNING BLOCK 1B · TOPIC 1
Implant Dose and Energy
1
Dose controls total implanted ions
Dose controls total implanted ions
2
Energy controls the depth distribution
Energy controls the depth distribution
3
Tilt and twist reduce channeling and shadowing
Tilt and twist reduce channeling and shadowing
4
Uniform scanning protects within-wafer consistency
Uniform scanning protects within-wafer consistency
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
43

## Slide 44
LEARNING BLOCK 1B · TOPIC 1
Beamline Risks
1
Charging can deflect beams or damage dielectrics
Charging can deflect beams or damage dielectrics
2
Channeling produces unexpectedly deep tails
Channeling produces unexpectedly deep tails
3
Mask topography creates shadowed regions
Mask topography creates shadowed regions
4
Beam focus and scan strategy affect uniformity
Beam focus and scan strategy affect uniformity
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
44

## Slide 45
LEARNING BLOCK 1B · TOPIC 1
Crystal Damage and Activation
WHAT CHANGES
1
Implant collisions create vacancies and interstitials
2
Anneal repairs lattice damage
WHAT TO VERIFY
1
Activation places dopants on useful sites
2
Electrical improvement can coexist with diffusion
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
45

## Slide 46
LEARNING BLOCK 1B · TOPIC 1
Diffusion, Furnace and RTP
1
Furnace cycles favour batch throughput and long soak
Furnace cycles favour batch throughput and long soak
2
RTP uses fast ramps and short dwell
RTP uses fast ramps and short dwell
3
Thermal budget controls activation and junction movement
Thermal budget controls activation and junction movement
4
The best cycle balances electrical target with geometry
The best cycle balances electrical target with geometry
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
46

## Slide 47
LEARNING BLOCK 1B · TOPIC 1
Thermal Oxidation
1
Silicon is consumed as silicon dioxide grows
Silicon is consumed as silicon dioxide grows
2
Dry oxidation grows slowly with strong film quality
Dry oxidation grows slowly with strong film quality
3
Wet oxidation grows faster for thicker films
Wet oxidation grows faster for thicker films
4
Temperature, time and surface condition control integrity
Temperature, time and surface condition control integrity
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
47

## Slide 48
LEARNING BLOCK 1B · TOPIC 1
CVD, PECVD and Epitaxy
CVD
film forms through surface reactions
PECVD
plasma lowers process temperature
Epitaxy
deposited crystal follows the substrate lattice
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
48

## Slide 49
LEARNING BLOCK 1B · TOPIC 1
PVD, Barrier and Seed
1
Sputtering transports target atoms to the wafer
Sputtering transports target atoms to the wafer
2
Directional coverage challenges deep features
Directional coverage challenges deep features
3
Barrier films limit metal diffusion
Barrier films limit metal diffusion
4
Continuous seed enables uniform electrofill
Continuous seed enables uniform electrofill
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
49

## Slide 50
LEARNING BLOCK 1B · TOPIC 1
Copper Dual Damascene
WHAT CHANGES
1
Pattern vias and trenches in dielectric
2
Deposit liner, barrier and seed
WHAT TO VERIFY
1
Electrofill copper without seams or voids
2
Polish overburden while protecting pattern density
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
50

## Slide 51
LEARNING BLOCK 1B · TOPIC 1
CMP Mechanics and Chemistry
1
Pad contact and slurry chemistry work together
Pad contact and slurry chemistry work together
2
Downforce, speed and pad state affect removal
Downforce, speed and pad state affect removal
3
Selectivity protects stop layers
Selectivity protects stop layers
4
Post-CMP clean removes abrasive and metal residue
Post-CMP clean removes abrasive and metal residue
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
51

## Slide 52
LEARNING BLOCK 1B · TOPIC 1
Planarity Failure Modes
1
Dishing removes too much metal in wide features
Dishing removes too much metal in wide features
2
Erosion lowers dense pattern regions
Erosion lowers dense pattern regions
3
Incomplete clear leaves conductive residue
Incomplete clear leaves conductive residue
4
Topography and electrical continuity must both pass
Topography and electrical continuity must both pass
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
52

## Slide 53
LEARNING BLOCK 1B · TOPIC 1
Integrated FEOL and BEOL
Isolation and wells define device regions
Isolation and wells define device regions
Gate and source/drain form transistors
Gate and source/drain form transistors
Contacts and interconnect create connectivity
Contacts and interconnect create connectivity
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
53

## Slide 54
LEARNING BLOCK 1B · TOPIC 1
Cross-Module Budgeting
1
Thermal budget accumulates across later steps
Thermal budget accumulates across later steps
2
Topography changes the next lithography window
Topography changes the next lithography window
3
Contamination transfers through surfaces and tools
Contamination transfers through surfaces and tools
4
Every hand-off needs evidence and an owner
Every hand-off needs evidence and an owner
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
54

## Slide 55
LEGACY VISUAL · SOURCE SLIDE 152
CMP Tool and Contact Mechanics
READ THE VISUAL
1
Locate wafer, pad and slurry interface
2
Connect relative motion to removal
3
Distinguish removal rate from final planarity
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
55

## Slide 56
LEGACY VISUAL · SOURCE SLIDE 195
FEOL and BEOL Cross-Sections
READ THE VISUAL
1
Separate transistor formation from interconnect
2
Read connectivity through contacts and vias
3
Identify module interfaces
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
56

## Slide 57
LEGACY VISUAL · SOURCE SLIDE 210
Shallow Trench Isolation Flow
READ THE VISUAL
1
Follow trench from pattern to fill
2
Locate etch, oxidation, deposition and CMP
3
Identify where active-area CD can move
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
57

## Slide 58
LEGACY VISUAL · SOURCE SLIDE 219
Wafer Sort as an Integration Gate
READ THE VISUAL
1
Test every die against criteria
2
Convert results into wafer-level patterns
3
Feed spatial signatures back to modules
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
58

## Slide 59
LEARNING BLOCK 1B · REAL-USE-CASE ACTIVITY
Balance Implantation and Thermal Budget
ACTIVITY 3
After a source/drain extension implant, sheet resistance is above target and short-channel control is drifting. The team must distinguish dose/energy error from activation and diffusion effects.
YOU'LL PRODUCE
Create an implant-to-anneal decision trail that balances activation, junction depth, damage recovery and channeling risk.
Full procedure: Learner Guide and individual activity folder
LO1 · 55 minutes
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
59

## Slide 60
ACTIVITY 3 · ANALYSE BEFORE DECIDING
Visual Brief and Evidence Lens
1
Which module interaction is most critical?
2
What evidence distinguishes competing causes?
3
Where is the hold/release gate?
4
What follow-up action closes the risk?
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
60

## Slide 61
ACTIVITY 3 · VERIFY
Acceptance Review
✓
The recommendation distinguishes implant dose/energy, damage and activation mechanisms.
✓
Thermal-budget effects on activation and diffusion are explicit.
✓
Follow-up measurements can confirm or reject the proposed cause.
Evidence: analysis output · completed checklist · measurement trail · decision and owner
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
61

## Slide 62
LEARNING BLOCK 1B · REAL-USE-CASE ACTIVITY
Integrate Film Deposition and CMP
ACTIVITY 4
A dual-damascene copper level meets line-resistance targets at wafer centre but fails near the edge with dishing, erosion and suspected barrier continuity loss.
YOU'LL PRODUCE
Trace deposition, fill and CMP interactions and design a verification plan that protects both planarity and electrical performance.
Full procedure: Learner Guide and individual activity folder
LO1 · 55 minutes
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
62

## Slide 63
ACTIVITY 4 · ANALYSE BEFORE DECIDING
Visual Brief and Evidence Lens
1
Which module interaction is most critical?
2
What evidence distinguishes competing causes?
3
Where is the hold/release gate?
4
What follow-up action closes the risk?
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
63

## Slide 64
ACTIVITY 4 · VERIFY
Acceptance Review
✓
The layer stack and each module's function are correctly labelled.
✓
The analysis distinguishes deposition/fill causes from polishing causes.
✓
The release rule uses both physical and electrical evidence.
Evidence: analysis output · completed checklist · measurement trail · decision and owner
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
64

## Slide 65
CHECK YOUR UNDERSTANDING
Block 1B Recap
1
Explain
CMP Mechanics and Chemistry
2
Explain
Planarity Failure Modes
3
Explain
Integrated FEOL and BEOL
4
Explain
Cross-Module Budgeting
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
65

## Slide 66
End of Day 1
Return ready to verify performance and control
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
66

## Slide 67
TOPIC 2 · LEARNING BLOCK 2A
Integration Performance, Yield and Reliability
Use metrology, electrical data and reliability evidence to verify product performance.
2A
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
67

## Slide 68
PART 1 · BUILD THE MODEL
Block 2A Roadmap
1
Isolation and Well Integration
Isolation and Well Integration
2
Transistor Formation
Transistor Formation
3
Yield Is Multiplicative
Yield Is Multiplicative
4
Defect Density and Die Area
Defect Density and Die Area
5
Metrology by Question
Metrology by Question
6
Measurement Strategy
Measurement Strategy
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
68

## Slide 69
PART 2 · VERIFY THE EVIDENCE
Block 2A Roadmap
1
Electrical Performance
Electrical Performance
2
Reliability Evidence
Reliability Evidence
3
HCI, TDDB and Electromigration
HCI, TDDB and Electromigration
4
Control Limits versus Specifications
Control Limits versus Specifications
5
Capability
Cp and Cpk
6
Evidence-Based Release
Evidence-Based Release
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
69

## Slide 70
BLOCK 2A · IMAGEGEN VISUAL
Integration Performance, Yield and Reliability in Practice
1
What module is creating the feature?
2
Which interaction can move device performance?
3
What measurement makes the decision defensible?
4
Where should feedback or containment occur?
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
70

## Slide 71
LEARNING BLOCK 2A · TOPIC 2
Isolation and Well Integration
1
LOCOS is simple but creates bird's-beak encroachment
LOCOS is simple but creates bird's-beak encroachment
2
STI supports scaling through etched and filled trenches
STI supports scaling through etched and filled trenches
3
Well architecture controls body regions
Well architecture controls body regions
4
Stress, CD and topography affect device behaviour
Stress, CD and topography affect device behaviour
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
71

## Slide 72
LEARNING BLOCK 2A · TOPIC 2
Transistor Formation
1
Gate stack sets electrostatic control
Gate stack sets electrostatic control
2
Source/drain implants establish junctions
Source/drain implants establish junctions
3
Spacers sequence extension and deep implants
Spacers sequence extension and deep implants
4
Contacts must preserve silicide and junction integrity
Contacts must preserve silicide and junction integrity
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
72

## Slide 73
LEARNING BLOCK 2A · TOPIC 2
Yield Is Multiplicative
WHAT CHANGES
1
Wafer-fab yield reflects process survival
2
Wafer-sort yield reflects functional die
WHAT TO VERIFY
1
Packaging yield reflects assembly and final test
2
One stage can erase gains made at another
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
73

## Slide 74
LEARNING BLOCK 2A · TOPIC 2
Defect Density and Die Area
1
Larger die expose more area to random defects
Larger die expose more area to random defects
2
Clustered defects violate simple random assumptions
Clustered defects violate simple random assumptions
3
Systematic defects need separate treatment
Systematic defects need separate treatment
4
Yield models support prediction, not proof
Yield models support prediction, not proof
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
74

## Slide 75
LEARNING BLOCK 2A · TOPIC 2
Metrology by Question
1
Ellipsometry
thin-film thickness and optics
2
Profilometry/AFM
step height and topography
3
SEM/TEM
CD, profile and internal structure
4
SIMS/Auger
concentration and surface composition
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
75

## Slide 76
LEARNING BLOCK 2A · TOPIC 2
Measurement Strategy
Before and after
isolate the suspected module
Spatial map
expose centre-edge or chamber signatures
Resolution
match instrument to the feature
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
76

## Slide 77
LEARNING BLOCK 2A · TOPIC 2
Electrical Performance
1
Four-point probe measures sheet resistance
Four-point probe measures sheet resistance
2
Gate-oxide integrity tests dielectric weakness
Gate-oxide integrity tests dielectric weakness
3
I-V curves reveal threshold, leakage and drive
I-V curves reveal threshold, leakage and drive
4
Product specifications decide pass/fail
Product specifications decide pass/fail
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
77

## Slide 78
LEARNING BLOCK 2A · TOPIC 2
Reliability Evidence
WHAT CHANGES
1
Mechanism explains degradation
2
Accelerated stress creates measurable change
WHAT TO VERIFY
1
Failure criterion defines the endpoint
2
Physical confirmation links failure to cause
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
78

## Slide 79
LEARNING BLOCK 2A · TOPIC 2
HCI, TDDB and Electromigration
1
Hot carriers damage the channel interface
Hot carriers damage the channel interface
2
TDDB accumulates dielectric damage over time
TDDB accumulates dielectric damage over time
3
Electromigration moves metal under current density
Electromigration moves metal under current density
4
Geometry, material and temperature change lifetime
Geometry, material and temperature change lifetime
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
79

## Slide 80
LEARNING BLOCK 2A · TOPIC 2
Control Limits versus Specifications
1
Control limits describe process behaviour
Control limits describe process behaviour
2
Specification limits describe product requirements
Specification limits describe product requirements
3
A stable process may still be off target
A stable process may still be off target
4
An in-spec point can signal a process shift
An in-spec point can signal a process shift
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
80

## Slide 81
LEARNING BLOCK 2A · TOPIC 2
Capability: Cp and Cpk
Cp compares specification width with spread
Cp compares specification width with spread
Cpk also reflects centering
Cpk also reflects centering
Capability follows stability assessment
Capability follows stability assessment
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
81

## Slide 82
LEARNING BLOCK 2A · TOPIC 2
Evidence-Based Release
1
Define the product requirement
Define the product requirement
2
Select physical and electrical evidence
Select physical and electrical evidence
3
Compare with limits and uncertainty
Compare with limits and uncertainty
4
Document disposition and follow-up
Document disposition and follow-up
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
82

## Slide 83
LEGACY CONCEPT · NATIVE REBUILD
Yield Models and Their Assumptions
Poisson
Y = exp(-A D0)
Random, independent defects; useful as a simple baseline.
Murphy
Y = [(1 - exp(-A D0)) / (A D0)]²
Allows defect density to vary across the wafer.
Negative binomial
Y = (1 + A D0 / α)^(-α)
Represents clustered defects through clustering factor α.
A = die area · D0 = defect density · Use measured yield patterns to test the model assumption.
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
83

## Slide 84
LEGACY VISUAL · SOURCE SLIDE 260
SEM Evidence
READ THE VISUAL
1
Read dimensions from the scale
2
Distinguish surface from cross-section imaging
3
Link the image to the process question
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
84

## Slide 85
LEGACY VISUAL · SOURCE SLIDE 279
Hot-Carrier Degradation
READ THE VISUAL
1
Locate the high-field drain region
2
Connect trapped charge to parameter shift
3
Identify stress and readout evidence
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
85

## Slide 86
LEGACY VISUAL · SOURCE SLIDE 294
Capability Is Spread plus Centering
READ THE VISUAL
1
Compare distribution with specifications
2
Separate potential from actual capability
3
Do not claim capability before stability
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
86

## Slide 87
LEARNING BLOCK 2A · REAL-USE-CASE ACTIVITY
Review an STI Integration Flow
ACTIVITY 5
TechSemicon is introducing shallow trench isolation for an advanced CMOS product. Electrical spread and active-area CD variation appear after integration, and the review board needs a complete process/evidence chain.
YOU'LL PRODUCE
Produce the process-flow and challenge analysis for a shallow trench isolation integration.
Full procedure: Learner Guide and individual activity folder
LO2 · 60 minutes
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
87

## Slide 88
ACTIVITY 5 · ANALYSE BEFORE DECIDING
Visual Brief and Evidence Lens
1
Which module interaction is most critical?
2
What evidence distinguishes competing causes?
3
Where is the hold/release gate?
4
What follow-up action closes the risk?
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
88

## Slide 89
ACTIVITY 5 · VERIFY
Acceptance Review
✓
The eight core STI stages are in the correct order and have a purpose.
✓
At least four implementation challenges are linked to measurements.
✓
The flow explains both scaling benefit and integration risk.
Evidence: analysis output · completed checklist · measurement trail · decision and owner
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
89

## Slide 90
LEARNING BLOCK 2A · REAL-USE-CASE ACTIVITY
Analyse Yield and Process Capability
ACTIVITY 6
A gate module has a target CD of 100 nm with specification limits at 90 and 110 nm. The process owner needs Cp/Cpk evidence and a reasoned yield-risk statement before qualification.
YOU'LL PRODUCE
Recreate and improve the legacy ProcessCapability exercise using an auditable Excel workbook with dynamic formulas.
Full procedure: Learner Guide and individual activity folder
LO2 · 75 minutes
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
90

## Slide 91
ACTIVITY 6 · ANALYSE BEFORE DECIDING
Visual Brief and Evidence Lens
1
Which module interaction is most critical?
2
What evidence distinguishes competing causes?
3
Where is the hold/release gate?
4
What follow-up action closes the risk?
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
91

## Slide 92
ACTIVITY 6 · VERIFY
Acceptance Review
✓
Workbook formulas remain intact and show no Excel errors.
✓
The learner distinguishes Cp from Cpk and links both to process evidence.
✓
The decision includes containment, corrective action and verification.
Evidence: analysis output · completed checklist · measurement trail · decision and owner
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
92

## Slide 93
CHECK YOUR UNDERSTANDING
Block 2A Recap
1
Explain
HCI, TDDB and Electromigration
2
Explain
Control Limits versus Specifications
3
Explain
Capability: Cp and Cpk
4
Explain
Evidence-Based Release
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
93

## Slide 94
Afternoon Break
10 minutes
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
94

## Slide 95
TOPIC 2 · LEARNING BLOCK 2B
SPC, Packaging and Future Integration
Control excursions, close the feedback loop and evaluate next-generation choices.
2B
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
95

## Slide 96
PART 1 · BUILD THE MODEL
Block 2B Roadmap
1
SPC as a Feedback System
SPC as a Feedback System
2
Select the Chart from the Data
Select the Chart from the Data
3
Variable Control Charts
Variable Control Charts
4
Attribute Control Charts
Attribute Control Charts
5
Signals Beyond One Point
Signals Beyond One Point
6
Excursion Response
Excursion Response
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
96

## Slide 97
PART 2 · VERIFY THE EVIDENCE
Block 2B Roadmap
1
Packaging Process Flow
Packaging Process Flow
2
Wire Bond and Flip Chip
Wire Bond and Flip Chip
3
2.5D, 3D and Chiplets
2.5D, 3D and Chiplets
4
FinFET
FinFET
5
GAAFET Nanosheets
GAAFET Nanosheets
6
Beyond Today's CMOS
Beyond Today's CMOS
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
97

## Slide 98
BLOCK 2B · IMAGEGEN VISUAL
SPC, Packaging and Future Integration in Practice
1
What module is creating the feature?
2
Which interaction can move device performance?
3
What measurement makes the decision defensible?
4
Where should feedback or containment occur?
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
98

## Slide 99
LEARNING BLOCK 2B · TOPIC 2
SPC as a Feedback System
1
Sample the process with a rational subgroup
Sample the process with a rational subgroup
2
Plot performance against behaviour-based limits
Plot performance against behaviour-based limits
3
Detect special-cause signals
Detect special-cause signals
4
Contain risk and restore control with evidence
Contain risk and restore control with evidence
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
99

## Slide 100
LEARNING BLOCK 2B · TOPIC 2
Select the Chart from the Data
1
Variable data
measurements such as CD
2
Attribute data
counts or proportions
3
Subgroup size decides Xbar-R versus Xbar-S
Subgroup size decides Xbar-R versus Xbar-S
4
Opportunity and sample size decide p, np, c or u
Opportunity and sample size decide p, np, c or u
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
100

## Slide 101
LEARNING BLOCK 2B · TOPIC 2
Variable Control Charts
WHAT CHANGES
1
Xbar tracks subgroup centre
2
R or S tracks within-subgroup spread
WHAT TO VERIFY
1
The two charts answer different questions
2
A mean chart is incomplete without spread
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
101

## Slide 102
LEARNING BLOCK 2B · TOPIC 2
Attribute Control Charts
1
p chart
proportion defective, variable sample size
2
np chart
defective count, constant sample size
3
c chart
defect count, constant opportunity
4
u chart
defects per unit, variable opportunity
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
102

## Slide 103
LEARNING BLOCK 2B · TOPIC 2
Signals Beyond One Point
1
A point beyond a limit is a strong signal
A point beyond a limit is a strong signal
2
Runs and trends expose non-random change
Runs and trends expose non-random change
3
Stratification reveals tool, wafer or time source
Stratification reveals tool, wafer or time source
4
Rules must be defined before interpretation
Rules must be defined before interpretation
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
103

## Slide 104
DECISION SEQUENCE · PROCEDURE IN LEARNER GUIDE
Excursion Response
1
Contain
Hold material and preserve evidence
2
Stratify
Tool, chamber, wafer, product and time
3
Correct
Controlled change with rollback criteria
4
Verify
Stable behaviour and capability
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
104

## Slide 105
LEARNING BLOCK 2B · TOPIC 2
Packaging Process Flow
1
Prepare and thin wafer
Prepare and thin wafer
2
Separate, inspect and attach die
Separate, inspect and attach die
3
Create electrical interconnect
Create electrical interconnect
4
Seal, plate, final-test and burn-in as required
Seal, plate, final-test and burn-in as required
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
105

## Slide 106
LEARNING BLOCK 2B · TOPIC 2
Wire Bond and Flip Chip
WHAT CHANGES
1
Wire bond is flexible but adds loop length
2
Flip chip raises I/O density
WHAT TO VERIFY
1
Underfill and joint quality manage mechanical risk
2
Inspection and test protect assembly yield
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
106

## Slide 107
LEARNING BLOCK 2B · TOPIC 2
2.5D, 3D and Chiplets
1
Interposers connect multiple dies
Interposers connect multiple dies
2
3D stacks use vertical connections
3D stacks use vertical connections
3
Known-good-die and thermal design are inputs
Known-good-die and thermal design are inputs
4
Integration control crosses organisations
Integration control crosses organisations
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
107

## Slide 108
LEARNING BLOCK 2B · TOPIC 2
FinFET
1
A fin raises the channel above substrate
A fin raises the channel above substrate
2
Multiple gate surfaces improve control
Multiple gate surfaces improve control
3
Fin geometry and parasitics affect performance
Fin geometry and parasitics affect performance
4
Patterning and variability challenge manufacturing
Patterning and variability challenge manufacturing
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
108

## Slide 109
LEARNING BLOCK 2B · TOPIC 2
GAAFET Nanosheets
Gate surrounds the channel
Gate surrounds the channel
Stacked sheets increase effective width
Stacked sheets increase effective width
Release, inner spacer and contacts are critical
Release, inner spacer and contacts are critical
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
109

## Slide 110
DECISION SEQUENCE · PROCEDURE IN LEARNER GUIDE
Technology Readiness Gate
1
Process
Capability and module interactions
2
Performance
Device metrics against target
3
Reliability
Stress evidence and failure criteria
4
Manufacturing
Yield, test and ownership
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
110

## Slide 111
LEGACY VISUAL · SOURCE SLIDE 349
Flip-Chip Interconnect
READ THE VISUAL
1
Trace die-to-substrate connections
2
Locate solder joints and underfill
3
Connect geometry to mechanical risk
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
111

## Slide 112
LEGACY VISUAL · SOURCE SLIDE 368
Chiplet Integration
READ THE VISUAL
1
Identify separate functional dies
2
Recognise substrate or interposer
3
Treat known-good-die and test as inputs
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
112

## Slide 113
LEGACY VISUAL · SOURCE SLIDE 371
FinFET Geometry
READ THE VISUAL
1
Read gate contact around the fin
2
Connect fin geometry to channel width
3
Identify geometry-sensitive modules
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
113

## Slide 114
LEGACY VISUAL · SOURCE SLIDE 372
GAAFET Nanosheet Geometry
READ THE VISUAL
1
See the gate surrounding each sheet
2
Compare stacked channel configurations
3
Identify release and spacer risk
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
114

## Slide 115
LEARNING BLOCK 2B · REAL-USE-CASE ACTIVITY
Respond to an SPC CD Excursion
ACTIVITY 7
STI active-area CD is drifting across production lots. A point crosses the upper control limit and a seven-point upward run appears before the alarm. The team must contain risk and restore control.
YOU'LL PRODUCE
Recreate the legacy P-chart/SPC exercises and generate the corrective-action chain for a CD excursion.
Full procedure: Learner Guide and individual activity folder
LO2 · 50 minutes
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
115

## Slide 116
ACTIVITY 7 · ANALYSE BEFORE DECIDING
Visual Brief and Evidence Lens
1
Which module interaction is most critical?
2
What evidence distinguishes competing causes?
3
Where is the hold/release gate?
4
What follow-up action closes the risk?
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
116

## Slide 117
ACTIVITY 7 · VERIFY
Acceptance Review
✓
The response identifies both limit violation and non-random pattern.
✓
Containment precedes root-cause adjustment and protects affected lots.
✓
Corrective action, verification criteria and follow-up owner are explicit.
Evidence: analysis output · completed checklist · measurement trail · decision and owner
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
117

## Slide 118
LEARNING BLOCK 2B · REAL-USE-CASE ACTIVITY
Run a Future-Technology Integration Gate
ACTIVITY 8
A product team is deciding whether to adopt chiplet packaging, FinFET or GAAFET for its next platform. Integration readiness must be assessed using process, performance, reliability and packaging evidence.
YOU'LL PRODUCE
Combine the entire course into a structured technology-gate recommendation without treating future devices as isolated marketing concepts.
Full procedure: Learner Guide and individual activity folder
LO2 · 50 minutes
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
118

## Slide 119
ACTIVITY 8 · ANALYSE BEFORE DECIDING
Visual Brief and Evidence Lens
1
Which module interaction is most critical?
2
What evidence distinguishes competing causes?
3
Where is the hold/release gate?
4
What follow-up action closes the risk?
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
119

## Slide 120
ACTIVITY 8 · VERIFY
Acceptance Review
✓
The recommendation integrates process, device, reliability, yield and packaging evidence.
✓
Every gate has a measurable threshold and an accountable follow-up action.
✓
The conclusion is conditional on evidence rather than technology hype.
Evidence: analysis output · completed checklist · measurement trail · decision and owner
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
120

## Slide 121
CHECK YOUR UNDERSTANDING
Block 2B Recap
1
Explain
2.5D, 3D and Chiplets
2
Explain
FinFET
3
Explain
GAAFET Nanosheets
4
Explain
Beyond Today's CMOS
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
121

## Slide 122
WRAP-UP
Integrated CMOS Decision Workflow
Process · interaction · evidence · performance · action
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
122

## Slide 123
CAPSTONE
The Complete Workflow
1
Identify technology flow
▶
2
Map module interactions
▶
3
Select performance evidence
▶
4
Verify against requirements
▶
5
Contain and follow up
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
123

## Slide 124
QUALITY GATE
Professional Integration Review
Process and evidence
1
Is the process sequence complete?
2
Which interaction creates the risk?
3
What incoming and outgoing evidence exists?
4
Are limits and uncertainty explicit?
Decision and ownership
1
Does performance meet product requirements?
2
Is the process stable and capable?
3
Is reliability evidence sufficient?
4
Who owns the next action and by when?
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
124

## Slide 125
SOURCE TRACEABILITY
Source and Evidence Register
1
Legacy v7 trainer deck retained as the content and visual coverage floor
2
Original graphics use aspect-ratio-safe contain placement
3
New Imagegen visuals are recorded in the source register
4
Detailed procedures remain in the Learner Guide and activity folders
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
125

## Slide 126
COURSE FEEDBACK
Course Feedback & Certificate
1
Complete the course feedback survey before you leave
2
Tell us what worked and what to improve
3
Ask the trainer if you cannot open the survey
4
Your certificate of completion will be emailed to you
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
126

## Slide 127
CMOS PROCESS INTEGRATION
Thank You
Integrate the flow, follow the evidence and close every risk with an accountable action.
Semiconductor Process Fundamentals · C716
© 2026 Tertiary Infotech Academy Pte Ltd
127